## Slide 1: Accurate Vehicle Localization: A Survey
ZHU Zhuangdi
Supervised by WANG Yi
Notes: Inertia navigation system, https://en.wikipedia.org/wiki/Inertial_navigation_system

## Slide 2: Outline
Motivation
Main Solutions
Examples
Future Trends

## Slide 3: Motivation
Application requirements vary

## Slide 4: Motivation
Inaccurate GPS-only localization
Source | Effect(m)
Signal arrival(C/A) | ±3
Signal arrival P(Y) | ±0.3
Lonospheric effects | ±5
Ephemeris errors | ±2.5
Satellite clock errors | ±2
Multipath distortion | ±1
Tropospheric effects | ±0.5
3σR C/A | ±6.7
3σR P(Y) | ±6.0
Source of User Equivalent Error Range[1]:
Error Analysis of GPS, https://en.wikipedia.org/wiki/Error_analysis_for_the_Global_Positioning_System

## Slide 5: Main Solutions
Absolute Localization
Single Vehicle Scenario
Relative Localization
Collaborative Vehicle Localization
State Estimation
INS
Particle Filtering
Kalman Filtering
Data Fusion
Multiple Sensors
Map/Satellite/Camera/Video based
Fault Correction
Multipath Detection
Differential GPS
GPS

## Slide 6: Example.1
Intervehicle-Communication-Assisted Localization[1]
Main Idea:
  GPS + INS + Kalman Filtering + Multipath Detection + Relative Localization
Drawil N M, Basir O. Intervehicle-communication-assisted localization[J]. Intelligent Transportation Systems, IEEE Transactions on, 2010, 11(3): 678-691.
Notes: Drawil N M, Basir O. Intervehicle-communication-assisted localization[J]. Intelligent Transportation Systems, IEEE Transactions on, 2010, 11(3): 678-691.

## Slide 7: Example.1
Intervehicle-Communication-Assisted Localization(IVCAL)[1]
System Architecture:
Drawil N M, Basir O. Intervehicle-communication-assisted localization[J]. Intelligent Transportation Systems, IEEE Transactions on, 2010, 11(3): 678-691.
GPS-INS Fusion Unit
Multipath Detection Unit(MDU)
Localization Enhancement Unit
IMU measurement
GPS Reading
IVCAL Estimate
Notes: Drawil N M, Basir O. Intervehicle-communication-assisted localization[J]. Intelligent Transportation Systems, IEEE Transactions on, 2010, 11(3): 678-691.

## Slide 8: Example.1
Intervehicle-Communication-Assisted Localization[1]
Steps:
Drawil N M, Basir O. Intervehicle-communication-assisted localization[J]. Intelligent Transportation Systems, IEEE Transactions on, 2010, 11(3): 678-691.
GPS-INS Fusion
Multipath Detection Unit(MDU)
Localization Enhancement Unit
Kalman Filtering
Feed Forward Back-propagation Network
Least Square Formulation(Relative Localization)
Notes: Drawil N M, Basir O. Intervehicle-communication-assisted localization[J]. Intelligent Transportation Systems, IEEE Transactions on, 2010, 11(3): 678-691.

## Slide 9: Example. 1
Step 1: GPS-INS Fusion
Prediction
Kalman Filtering：Prediction & Update
Update/Filter:

## Slide 10: Example. 1
Step 2: Multipath Detection
Input Pattern(Discrepancy between measurement & estimate )
……..
Information Flow
Neuron
Multipath Effect :Yes/No
Input Layer
Hidden Layer
Output Layer

## Slide 11: Example. 1
  Step 3: Localization Enhancement/Update

## Slide 12: Example. 1
In paper:
Maybe:
  Step 3: Localization Enhancement/Update

## Slide 13: Example. 1
Conclusion
No. | Contributions | Drawbacks
1 | Inter-vehicle location correction | Inaccurate Anchor Locations & Relative Distance -> accumulated error
2 | ANN based Fault Detection | Insufficient Anchor Nodes( < 3 scenario)

## Slide 14: Example. 2
Map-Based Precision Vehicle Localization in Urban Environments[1]
Main Idea:
  GPS + Map Matching + INS + Particle Filtering
1. Levinson J, Montemerlo M, Thrun S. Map-Based Precision Vehicle Localization in Urban Environments[C]//Robotics: Science and Systems. 2007, 4: 1.
Notes: 1. Levinson J, Montemerlo M, Thrun S. Map-Based Precision Vehicle Localization in Urban Environments[C]//Robotics: Science and Systems. 2007, 4: 1.

## Slide 15: Example. 2
Fig.1. Mapping
Fig. 2. Localization
Steps
  Mapping & Localization

## Slide 16: Example.2
Steps
Mapping
Localization
Techniques
LIDAR Mapping
GPS
INS
Particle Filtering
Steps
  Mapping
    Using LIDAR to
    build 2-D maps
  Localization
    Real time GPS
    localizing relative to
    previously created maps
    Using particle filtering to
    predict and update
    vehicle locations

## Slide 17: Example. 2
Mapping
  Mapping Technique:
    GraphSLAM[1] + LIDAR
  Map representation:
    2-D surface image
    5cm pixel resolution.
  Map matching:
    Identify regions of overlap
Mapping
Localization
SLAM, wikipedia, https://en.wikipedia.org/wiki/Simultaneous_localization_and_mapping
Notes: which assigns to each x-y location in the environment an infrared reflectivity value
Visualization of the scanning process: the LIDAR scanner acquires range data and infrared ground reflectivity. The resulting maps therefore are 3-D infrared images of the ground reflectivity. Notice that lane markings have much higher reflectivity than pavement.

## Slide 18: Example. 2
Localization
  IMU[1] + GPS + Particle Filtering[2]
1. Bayesian Filtering: From Kalman Filters to Particle Filters, and Beyond (2003) by Zhe Chen
2. Inertial Measurement Unit, wikipedia, https://en.wikipedia.org/wiki/Inertial_measurement_unit
Prior Estimated Value X’k
Posterior Estimated Value Xk
Last State Estimated Value Xk-1
Prediction
Particle Filtering
Filtering/Updating
Iteration
Mapping
Localization
Motion Model
Weighted Resampling
IMU Parameters
GPS Measurement
Notes: which assigns to each x-y location in the environment an infrared reflectivity value
Visualization of the scanning process: the LIDAR scanner acquires range data and infrared ground reflectivity. The resulting maps therefore are 3-D infrared images of the ground reflectivity. Notice that lane markings have much higher reflectivity than pavement.

## Slide 19: Example. 2
  Conclusion
No. | Contributions | Drawbacks
1 | High resolution map | Offline map resolution relaxation
2 | Centimeter Accuracy | Map store & management overhead
3 | Able to process particle filter without GPS | Hardware costs
4 |  | Time delay on mapping and localization (a few seconds)

## Slide 20: Future Trends
GPS/INS + Location Estimate
Inter-vehicle assisted Localization for Location update and error correction
Fault detection using neural networks
Particle Filtering…
TOA, AOA, RSSI
Trilateration…
  FFBN in multipath detection…

## Slide 21
Thank You

## Slide 22: References
iOnRoad, an android vehicle safety APP, http://v.youku.com/v_show/id_XMzEzODI1MzIw.html
Boukerche A, Oliveira H A B F, Nakamura E F, et al. Vehicular ad hoc networks: A new challenge for localization-based systems[J]. Computer communications, 2008, 31(12): 2838-2849.
Schreiber M, Knoppel C, Franke U. Laneloc: Lane marking based localization using highly accurate maps[C]//Intelligent Vehicles Symposium (IV), 2013 IEEE. IEEE, 2013: 449-454
Najjar E, El Badaoui M, Bonnifait P. Road selection using multicriteria fusion for the road-matching problem[J]. Intelligent Transportation Systems, IEEE Transactions on, 2007, 8(2): 279-291.
Khattab A, Fahmy Y A, Wahab A A. High accuracy GPS-Free vehicle localization framework via an INS-Assisted single RSU[J]. International Journal of Distributed Sensor Networks, 2015, 2015: 71.
J. Rife, Collaborative vision-integrated pseudorange error removal: team-estimated differential GNSS corrections with no stationary reference receiver, IEEE Transactions on Intelligent Transportation Systems, vol.13, no.1, pp.15-24, March 2012
W. Li and H. Leung, Simultaneous registration and fusion of multiple dissimilar sensors for cooperative driving, IEEE Transactions on Intelligent Transportation Systems, vol.5, no.2, pp. 84- 98, June 2004
M. Woo, J. Choi, H. Han, Carrier phase GPS/millimeter-wave radar for vehicle platooning, IEEE Proc. of the Int. Symp. on Industrial Electronics (ISIE), vol.3, pp.1548-1552 vol.3, 2001.
G. Challita, S. Mousset, F. Nashashibi and A. Bensrhair, An application of V2V communications : cooperation of vehicles for a better car tracking using GPS and vision systems, IEEE Vehicular Networking Conference (VNC), pp.1-6, 28-30 Oct. 2009.
Obst M, Bauer S, Wanielik G. Urban multipath detection and mitigation with dynamic 3D maps for reliable land vehicle localization[C]//Position Location and Navigation Symposium (PLANS), 2012 IEEE/ION. IEEE, 2012: 685-691.

## Slide 23: Main Solutions
Absolute Localization
Single Vehicle Scenario
Relative Localization
Collaborative Vehicle Localization
State Estimation
INS
Particle Filtering
Kalman Filtering
Data Fusion
Multiple Sensors
Map/Satellite/Camera/Video based
Fault Correction
Multipath Detection
Differential GPS
GPS

## Slide 24: Main Solutions
Differential Global Positioning System(DGPS)
  Reference station with accurately-surveyed position
  Receivers/Rovers have to be enabled for DGNSS
  Rovers should be in vicinity of the reference station.
  Set up and calibration cost
  The roving receivers must remain stationary at each measurement point for a length of time in order to collect the appropriate amount of data.
Satellite-Based Augmentation System/Wide- Area Augmentation System (WAAS)
  WAAS gives actual estimates for the contributions of individual error sources in- stead of lumping them together: WAAS serves larger area than DGPS, and the error may not be correlated.
Inertial Navigation System(INS)
Real Time Kinematic Positioning
  RTK algorithms are necessarily carrier-phase based and always provide instantaneous and continuous receiver coordinates
  stationary reference node.
  consistent locks on at least three satellites
Map-matching
Multipath Detection