## Slide 1: Vehicular Ad Hoc Networks: A Survey
Zhuangdi Zhu

## Slide 2: Agenda
Introduction & Motivation
Research Fields
Open Questions & Challenges
Future Works

## Slide 3: Introduction & Motivation
Basic concepts of VAET
  An Variation of Mobile Ad Hoc Network(MANET)
V2I
V2V
V2X
MANET
VENET/V2V/
IVC

## Slide 4: Introduction & Motivation
Similarities with MANET
  No fixed Infrastructure
  Self-organization/management
VANET Features
  Highly Dynamic Topology
  Frequent Disconnection
  Geographical type of communication
  Hard Delay Constraints
  Sufficient Energy and Computing Resource
  Interaction with on-board sensors

## Slide 5: Introduction & Motivation
Motivation
  Safety
  Mobility
  Environment

## Slide 6: Introduction & Motivation
Nation/Area | USA | Europe | Japan/China
System Focus | V2V safety | V2I Mobility | V2V & V2I Safety & Mobility
Organization & Projects | PATH[2], ITS[3 | C2C CC[27], SAFESPOT[4], FleetNet[40] | ITS in Japan[5], CCSA in China[6]

## Slide 7: Research Issues
VANET PHY/MAC Layer
VANET Application Layer
  Comfort Applications
  Safety Applications
VANET Networking
  Routing Protocols
  Internet Connectivity
  Data Dissemination
  QoS Support
  Security & Privacy
  Model & Simulation

## Slide 8: Research Issues
VANET PHY/MAC Layer
  Physical Layer
    Radio, infrared, VHF, millimeter wave
    IEEE 802.11 a, b, g or p technology
      Minor solutions not based on IEEE 802.11[11]

## Slide 9: Research Issues
VANET PHY/MAC Layer
  Physical Layer
Nation/Area | USA | Europe | Japan/China
Broadcasting Frequency | 5.9 GHz, 70 MHz Spectrum | 5.9 GHz, 70 MHz Spectrum | 5.8 GHz
Wireless Protocol | IEEE Standard 802.11p | IEEE Standard 802.11p | IEEE Standard 802.11p
DSRC Protocol | IEEE 1609 | IEEE 1609 | ARIB STD-T75

## Slide 10: Research Issues
VANET PHY/MAC Layer
  Physical Layer
    Network Architecture
      WLAN/Cellular
      Ad Hoc
      Hybrid
        Namboodiri[7]
      (add three pictures here)

## Slide 11: Research Issues
VANET PHY/MAC Layer
  MAC Layer
    Random protocols(CSMA-like) are preferable to controlled ones(TDMA-like)
      DSRC
      FleetNet

## Slide 12: Research Issues
VANET Application Layer
  Comfort Applications(User applications)
    Awareness based
    Internet connectivity & peer-to-peer applications
  Safety Applications (Intelligent transportation applications)
    Event based
    Broadcast safety messages (collision warning, blind spot warning & lane change warning)

## Slide 13: Research Issues
VANET Networking
  Routing Protocols[8]
    Proactive & Reactive[17]

## Slide 14: Research Issues
VANET Networking
  Routing Protocols[8]
    Safety applications: broadcast routing schemes.
      require stringent time constraints on reaction time
    Comfort applications: unicast or multicast schemes.
      requirements have not be clearly defined.

## Slide 15: Research Issues
VANET Networking
  Routing Protocols[8]
    Unicast Routing
      OLSR[], AODV[], DSR[], …
    Multicast Routing
      [examples here]
    Broadcast Routing
      OLSR[] may be used to broadcast emergency in VANETs.

## Slide 16: Research Issues
VANET Networking
  Routing Protocols[8]
    Topology based (Ad hoc routing)[9]
    Position based (Geographical routing)[10]
      C2C CC uses geographic routing schemes[27]
      //Conditional transmission[26] is a generalization of this technology
      Scale well with dynamic network
      Optimizing routing path[18]
      More studies in need
    Cluster based
    Geocast

## Slide 17: Research Issues
VANET Networking
  Routing Protocols[8]
    AODV, DSR;PRAODV; LAR
    GPSR, GSR; GPCR; A-STAR
    COIN[]; LORA_CBF[]
    Flooding; BROADCOMM, V-TRADE, HV-TRADE
    (Location based, multicast routing) IVG
    (Give a table or graph here covering most protocols above)

## Slide 18: Research Issues
VANET Networking
  Internet Connectivity
    Vehicles within a network
      Use multi-homed vehicles as gateways[24]
      Use infrastructure gateways[]
    Vehicles Crossing networks
      [25]

## Slide 19: Research Issues
VANET Networking
  Data Dissemination:
    Cannot use group address but node positions
    Safety applications: broadcast within a zone under all conditions
      Either use hop counts[28] or use vehicle location info[29]
      No comparison studies exist and further investigation is in need .
    Comfort application:
      Use infrastructure support [30]
      Build completely independent peer-to-peer system[31]

## Slide 20: Research Issues
VANET Networking
  Security [10]: Contradictory properties
    Authentication & Liability
      Masquerade attack & denial of behavior
    Privacy & Anonymity
      Eaversdrop
      Leakage of identity info (location & movement patterns)

## Slide 21: Research Issues
VANET Networking
  Security [10]: Schemes
    Certification Authorities(CAs)
      The issue of certificate revocation[35]
    Use Keys
      Use pseudonym to improve privacy[33][34]
      Use asymmetric cryptography for safety message

## Slide 22: Research Issues
VANET Networking
  Security: the Status Quo
    Lack of specification for a real security system
    Lack of performance evaluation

## Slide 23: Research Issues
VANET Networking
  QoS Support
    Accuracy(corruption/collision) & efficiency(Broad Storm)
    Re-broadcast to achieve reliability[14]
    Change the transmission range of the emergency messages[15]

## Slide 24: Research Issues
VANET Networking
  Model & Simulation
    Normal Schemes:
      Output (trace files) can be used as input for a network simulator (NS-2/3)[38]
      Integrate with network simulator[37]

## Slide 25: Research Issues
VANET Networking
  Model & Simulation
    Earliest model:
      Random WayPoint (RWP)[36]
    Using realistic road map info
      Street Random WayPoint[37]
    Using realistic vehicular trace data[38][39]

## Slide 26: Research Issues
VANET Networking
  Model & Simulation
    The Status Quo:
      An integrated simulator to couple traffic and networks is in need.

## Slide 27: Open Questions
Scalability of VANET
  Bandwidth limitations, processing power, transmission frequency
  A long way to go to achieve high take-up level
How to Cope with Sparse and Partitioned Network in Initial Deployment?
  Use mobility to counterbalance sparsity[21]
    Require GPS and map info
  Existing solutions in MANET may help [22]

## Slide 28: Open Questions
How to Re-design IP Stacks for VANET Networks?
  TCP/IP Stack is designed for wired network and is inadequate for MANET or VANET[32].
  CB MANET aims to build completely new IP Stacks[23].
How to Reach a Consensus on Other Stacks?
  TCP/IP is ubiquitous.
  Applications for VANETs have not been clearly defined yet.

## Slide 29: Open Questions
How to Cope with High Node Density?
  Traffic jam or accident happens
  Solutions in wired network cannot handle spatial reuse
  Slotted approaches [12][13]
How to guarantee Connectivity?
  Connectivity is a real challenge due to high mobility of nodes
    Parition and merge of networks due to high mobility of nodes
    Predicting and message queuing [19][20]
    Mobility increases throughput in MANET[15]
How to support Time-Critical Traffic?
  Current WLAN solutions have no time constraints
  Broadcast storm during transmitting emergency message
  Existing solutions(Number, rate, range)
    Rebroadcast to achieve reliability[14]
    Change the transmission range of the emergency messages[15]

## Slide 30
Thank You

## Slide 31: References
“Vehicle-to-Vehicle”, https://en.wikipedia.org/wiki/Vehicle-to-vehicle
“PATH,” www.path.berkeley.edu
“USDoT ITS program,” www.its.dot.gov/factsheets/connected_vehicles_work.htm
“SAFESPOT,” www.safespot-eu.org
“ComprehensivePlanforITSinJapan”, www.mlit.go.jp/road/ITS/topindex/topindex_g06_2.html
“China ITS Industry Alliance”, http://www.c-its.org/
http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=4450627&url=http%3A%2F%2Fieeexplore.ieee.org%2Fxpls%2Fabs_all.jsp%3Farnumber%3D4450627
Hybrid VANET Network…
Routing: Ad Hoc …
http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=1306972&url=http%3A%2F%2Fieeexplore.ieee.org%2Fiel5%2F8013%2F29015%2F01306972
H. Hartenstein et al., “Position-Aware Ad Hoc Wireless Net- works for Inter-Vehicle Communications: The FleetNet Project,” MobiHoc ’01: Proc. 2nd ACM Int’l. Symp. Mobile Ad Hoc Net- working & Computing, New York: ACM Press, 2001, pp. 259–62.
https://users.ece.cmu.edu/~sazimi/SAE2011.pdf

## Slide 32: References
J. Blum, “Adaptive Space Division Multiplexing: An Improved Link Layer Protocol for Inter-Vehicle Communication,” IEEE Int’l. Conf. WiMob 2005, vol. 3, 2005, pp. 22–24.
K. Dobashi, “Adaptive MAC Protocol for High-Load Inter- Vehicle Communication,” Wireless and Mobile Computing, Networking and Commun. Mag., vol. 44, no. 1, 2006, pp. 74–82.
L. Liu et al., “A Vehicle-to-Vehicle Communication Protocol for Cooperative Collision Warning,” 1st Annual Int’l. Conf. Mobile and Ubiquitous Systems: Networking and Services, MOBIQUITOUS 2004.
M. Torrent-Moreno, P. Santi, and H. Hartenstein, “Fair Shar- ing of Bandwidth in VANETs,” Vehicular Ad Hoc Networks, 2005.
M. Grossglauer and D. N. C. Tse, “Mobility Increases the Capacity of Ad Hoc Wireless Networks,” IEEE/ACM Trans. Net., vol. 10, no. 4, 2002, pp. 477–86.
L. Viennot, P. Jacquet, and T. Clausen, “Analyzing Control Traffic Overhead Versus Mobility and Data Traffic Activity in Mobile Ad-Hoc Network Protocols,” Wireless Networks, vol. 10, no. 4, 2004, pp. 447–55.
I. Stojmenovic and X. Lin, “Power-Aware Localized Routing in Wireless Networks,” IEEE Trans. Parallel and Distributed Sys- tems, vol. 12, no. 11, 2001, pp. 1122–33.
K. Wu and J. Harms, “Performance Study of Proactive Flow Handoff for Mobile Ad Hoc Networks,” Wireless Networks, vol. 12, no. 1, 2006, pp. 119–35.
H. Menouar, M. Lenardi, and F. Filali, “Improving Proactive Routing in VANETs with the MOPR Movement Prediction Framework,” Proc. 7th Int’l. Conf. Intelligent Transport Sys- tems, 2007, pp. 438–43.
H. Wu, R. Fujimoto, R. Guensler, and M. Hunter, “MDDV: A Mobility-Centric Data Dissemination Algorithm for Vehicular Networks,” Vehicular Ad Hoc Networks, 2004.

## Slide 33: References
M. M. B. Tariq, M. H. Ammar, and E. W. Zegura, “Message Ferry Route Design for Sparse Ad Hoc Networks with Mobile Nodes,” MobiHoc, 2006, pp. 37–48.
“Control-Based Mobile Ad-Hoc Networking Program,” 2005; http://www.darpa.mil/sto/solicitations/CBMANET
V. Namboodiri, M. Agarwal, and L. Gao, “A Study on the Feasibility of Mobile Gateways for Vehicular Ad-Hoc Net- works,” Proc. VANET’04, 2004.
R. Wakikawa et al., “Design of Vehicle Network: Mobile Gate- way for MANET and NEMO Converged Communication,” Proc. 2nd ACM Int’l. Wksp. Vehicular Ad Hoc Networks, ACM Press, 2005, pp. 81–82.
B. Ducourthial, Y. Khaled, and M. Shawky, “Conditional Transmissions: A Strategy for Highly Dynamic Vehicular Ad Hoc Networks,” Heudiasyc lab. UMR CNRS 6599, Université de Technologie de Compiégne, Tech. Rep., 2006.
“Car 2 Car,” http://www.car-to-car.org
J. Bransted and L. M. Kristensen, “Specification and Performance Evaluation of Two Zone Dissemination Protocols for Vehicular Ad-Hoc Networks,” anss, vol. 0, 2006, pp. 68–79.
R. Fracchia, “Knowing Vehicles Location Helps Avoiding Broadcast Packets Storm,” PerCOMW, vol. 0, 2006, pp. 118–23.

## Slide 34: References
S. Ghandeharizade, S. Kapadia, and B. Krishnamachari, “PAVAN: A Policy Framework for Content Availability in Vehicular Ad-Hoc,” Vehic. Ad Hoc Networks, 2004.
T. Repantis and V. Kalogeraki, “Data Dissemination in Mobile Peer-to-Peer Networks,” Mobile Data Management, 2005.
Revealing TCP Unfairness Behavior in 802.11 Based Wireless Multi-Hop Networks, vol. 2, 2001.
P. Papadimitratos et al., “Architecture for Secure and Private Vehicular Communications,” Proc. 7th Int’l. Conf. Intelligent Transport Systems, 2007, pp. 339–34.
J. Freudiger et al., “Mix-Zones for Location Privacy in Vehicu- lar Networks,” WiN-ITS, 2007.
S. Miscali, “Efficient Certificate Revocation, MIT Laboratory for Computer Science, “ Tech. Rep. TM-542b, Mar. 1996, Tech. Rep.
J. Broch, D.A. Maltz, D.B. Johnson, Y.-C. Hu, and J. Jetcheva, “A performance comparison of multi-hop wireless ad hoc network routing protocols,” in Mobile Computing and Networking, pp. 85–97, 1998.
“U.S. Census Bureau. TIGER, TIGER/Line and TIGER-Related Products,” http://www.census.gov/geo/www/tiger/.
H. Füßler, M. Torrent-Moreno, M. Transier, R. Krüger, H. Hartenstein, and W. Effelsberg, “Studying vehicle movements on highways and their impact on ad- hoc connectivity,” in ACM Mobicom 2005, Aug. 2005.
V. Naumov, R. Baumann, and T. Gross, “An evaluation of inter-vehicle ad hoc networks based on realistic vehicular traces,” in MobiHoc ’06: Proceedings of the 7th ACM International Symposium on Mobile Ad Hoc Networking and Computing, pp. 108–119, 2006.
H. Hartenstein et al., “Position-Aware Ad Hoc Wireless Net- works for Inter-Vehicle Communications: The FleetNet Project,” MobiHoc ’01: Proc. 2nd ACM Int’l. Symp. Mobile Ad Hoc Net- working & Computing, New York: ACM Press, 2001, pp. 259–62.

## Slide 35
WAVE management

## Slide 36
USA V2V | Europe V2I | China & Japan V2V&V2I
PATH[2], ITS[3] Awareness-based Improve safety | C2C CC27] SAFESPOT[4], FleeNet[40] Event-based Improve Mobility | Japan: JSK[5] China: CCSA[6] …

## Slide 38: Developments & Standards
Nation/Area | USA | Europe | Japan/China
System Focus | V2V safety | V2I Mobility | V2V & V2I Safety & Mobility
Organization & Projects | PATH[2], ITS[3 | SAFESPOT[4], FleeNet[40] | ITS in Japan[5], CCSA[6]

## Slide 39: Introduction & Motivation
Basic concepts of VAET
  An Variation of Mobile Ad Hoc Network(MANET)
  Known as IVC or V2V
  Titled as V2X collectively with V2I
  Key Components of Intelligent Transportation System(ITS)