## Slide 1: Vehicular Ad Hoc Networks: A Survey
Zhuangdi Zhu

## Slide 2: Agenda
Introduction & Motivation
Research Fields
Questions & Challenges
Future Works

## Slide 3: Introduction & Motivation
What Is VANET [1]
  An Variation of Mobile Ad Hoc Network(MANET)[2].
V2I
V2V
V2X
MANET
VENET/V2V
Notes: “Vehicle-to-Vehicle”, https://en.wikipedia.org/wiki/Vehicle-to-vehicle
“Mobile Ad Hoc Network”,https://en.wikipedia.org/wiki/Mobile_ad_hoc_network

## Slide 4: Introduction & Motivation
Nation/Area | USA | Europe | Japan/China
System Focus | V2V safety | V2I Mobility | V2V & V2I Safety & Mobility
Organization & Projects | PATH[1], ITS[2] | C2C CC[6], SAFESPOT[3], FleetNet[7] | ITS in Japan[4], CCSA in China[5]
The Status Quo of VANET
Notes: “PATH,” www.path.berkeley.edu
“USDoT ITS program,” www.its.dot.gov/factsheets/connected_vehicles_work.htm
“SAFESPOT,” www.safespot-eu.org
“ComprehensivePlanforITSinJapan”, www.mlit.go.jp/road/ITS/topindex/topindex_g06_2.html
“China ITS Industry Alliance”, http://www.c-its.org/
“Car 2 Car,” http://www.car-to-car.org
H. Hartenstein et al., “Position-Aware Ad Hoc Wireless Net- works for Inter-Vehicle Communications: The FleetNet Project,” MobiHoc ’01: Proc. 2nd ACM Int’l. Symp. Mobile Ad Hoc Net- working & Computing, New York: ACM Press, 2001, pp. 259–62.

## Slide 5: Introduction & Motivation
Motivation
Safety
Mobility
Environment

## Slide 6: Introduction & Motivation
VANET Features
Highly Dynamic Topology
Availability of Geographical Position
Predictability of Vehicle movements
Hard Delay Constraints

## Slide 7: Research Fields
I
Physical Layer
Networking Services
WAVE Model
LLC SubLayer
MAC SubLayer
Application, Presentation, Session
Physical Layer
Data Link Layer
Transport Layer
Network Layer
OSI Model
Upper Layers
Safety App
Comfort App
Routing Protocols
QoS Support
Mobility Model & Simulation
Security
IEEE 802.11 P
IEEE 1609.1
& Applications
IEEE 1609.3
IEEE 1802.2
IEEE 1609.4
IEEE 1802.11
MAC Layer Issue
Physical Layer Issue

## Slide 8: Research Fields
Physical Layer
  Technology :
    Radio, infrared, VHF,
    millimeter wave
  Standards:
    IEEE 802.11 a, b, g or p technology[1]
    Minor solutions not based on IEEE 802.11[2]
Physical Layer
Networking Services
LLC SubLayer
MAC SubLayer
Upper Layers
Notes: “IEEE 802.11”, https://en.wikipedia.org/wiki/IEEE_802.11
H. Hartenstein et al., “Position-Aware Ad Hoc Wireless Net- works for Inter-Vehicle Communications: The FleetNet Project,” MobiHoc ’01: Proc. 2nd ACM Int’l. Symp. Mobile Ad Hoc Net- working & Computing, New York: ACM Press, 2001, pp. 259–62.

## Slide 9: Research Fields
Nation/Area | USA | Europe | Japan/China
Broadcasting Frequency | 5.9 GHz, | 5.9 GHz | 5.8 GHz
Wireless Protocol | IEEE Standard 802.11p | IEEE Standard 802.11p | IEEE Standard 802.11p
DSRC[1] Protocol | IEEE 1609 | IEEE 1609 | ARIB STD-T75 [2]
Physical Layer
  Current Standards
Notes: “Dedicated Short Range Communicaions”, https://en.wikipedia.org/wiki/Dedicated_short-range_communications
“Association of Radio Industry and Business”, http://www.arib.or.jp/english/

## Slide 10: Research Fields
Physical Layer
  Architecture Classfication
(1) Ad Hoc
(2) WLAN/Cellular
(3) Hybrid

## Slide 11: Research Fields
MAC Layer
  MAC Layer [1]:
    Goal: Time & space sharing
    Main schemes:
      Contention-free protocols [2]:
        CDMA, FDMA, TDMA
        Example: FleetNet -> slotted Aloha
        TDMA Scheme:
          Require RSUs to create and manage the
            TDMA slot reservation schedule.
          Require real-time system(GPS) for location
            and time information
      Contention-based protocols [3]:
        CSMA, ECDA, CSMA/CA
        Example: IEEE 802.11 P -> ECDA + CSMA/CA
Physical Layer
Networking Services
LLC SubLayer
MAC SubLayer
Upper Layers
Notes: D. Bertsekas and R. Gallager, Data Networks, Prentice-Hall, 2001.
Hadded M, Muhlethaler P, Laouiti A, et al. TDMA-Based MAC Protocols for Vehicular Ad Hoc Networks: A Survey, Qualitative Analysis, and Open Research Issues[J]. Communications Surveys & Tutorials, IEEE, 2015, 17(4): 2461-2492.
IEEE Standard for Information Technology— Telecommunications and Information Exchange Between Systems—Local and Metropolitan Area Networks—Specific Requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) and Physical Layer (PHY) Specifications Amendment 6: Wireless Access in Vehicular Envi- ronments, Std. 802.11p-2010, 2010.

## Slide 12: Research Fields
Upper Layers:
  Safety applications[1]
    Event Based
    Notify emergency messages
    Broadcast scheme
  Comfort Applications
    Awareness based
    Internet connectivity
    Peer-to-peer communication
    Unicast or multicast schemes
Physical Layer
Networking Services
LLC SubLayer
MAC SubLayer
Upper Layers
Notes: J. Harding et al., “Vehicle-to-vehicle communications: Readiness of V2V technology for application,” Nat. Highway Traffic Safety Admin., Washington, DC, USA, Tech. Rep. DOT HS 812 014, Aug. 2014.

## Slide 13
Emergency Brake Warning
Forward Collision Warning
Intersection Movement Assist
Blind Spot and Lane Change Warning
Do not Pass Warning
Safety Applications
Music Downloading
Back-seat Games
…
Comfort Applications

## Slide 14: Research Fields
Networking Services
  Routing Protocols
    Proactive & Reactive[17]
Physical Layer
Networking Services
LLC SubLayer
MAC SubLayer
Upper Layers
Routing Protocols
QoS Support
Mobility Model & Simulation

## Slide 15: Research Fields
Networking Services
  Routing Protocols:
    Transmission strategies based classification
Routing Protocols
Unicasting
Multicasting
Broadcasting
    Routing Information based classification
Routing Protocols
Topology based
Position based

## Slide 16: Research Fields
Networking Services
  Routing Protocols:
    Broadcasting[1]
Broadcasting Type | Characteristics | Advantages | Disadvantages
Multi-hop | Smart flooding Probability/ delay based | Low latency No need for large storage space | Broadcast storm No persistency
Single-hop | Periodic broadcast Vary broadcast interval Rely on node mobility | Persistency No broadcast storm | Slow Large storage space
Notes: Panichpapiboon S, Pattara-Atikom W. A review of information dissemination protocols for vehicular ad hoc networks[J]. Communications Surveys & Tutorials, IEEE, 2012, 14(3): 784-798.

## Slide 17: Research Fields
Broadcasting
Multi-hop
Single-hop
Delay
Probabilistic
Network Coding
Fixed Broadcast Interval
Adaptive Broadcast Interval
Networking Services
  Routing Protocols:
    Broadcast [1]
UMB
SB
EDB
…
Weighted
p-persistence
OAPB
AutoCast
…
CODEB
EBCD
DifCode
…
TrafficInfo
TrafficView
…
CRCP
Abiding Geocast
SODAD
…
Notes: Panichpapiboon S, Pattara-Atikom W. A review of information dissemination protocols for vehicular ad hoc networks[J]. Communications Surveys & Tutorials, IEEE, 2012, 14(3): 784-798.

## Slide 18: Research Fields
Networking Services
  Routing Protocols:
    Multicast[1]
Multicast Routing
Tree Based
Mesh Based
Group Forwarding Based
Core Based
AMRoute
ODMRP
CAMP
ODMRP
CTB
AMRIS
Notes: Patel B, Shah K. A Survey on Vehicular Ad hoc Networks[J]. IOSR Journal of Computer Engineering (IOSR-JCE) Vol, 2013, 15: 34-42.

## Slide 19: Research Fields
Networking Services
  Routing Protocols
    Unicast[1]
Notes: 1. J. Bernsen and D. Manivannan, “Unicast routing protocols for vehicular ad hoc networks: A critical comparison and classification,” Pervasive and Mobile Computing, vol. 5, no. 1, pp. 1–18, Feb. 2009.

## Slide 20: Research Fields
Networking Services
  Routing Protocols: Transmission strategies based classification[1]
Transmission Strategies |  | Communication Type | Example | Advantages | Disadvantages
Unicasting |  | One-to-one | AODV, DSR, GPSR | Less network Overhead More privacy | Less reliable Link maintenance
Broadcasting |  | One-to-all inside broadcast domain | BROADCOMM, DV-CAST | Reliable | Bandwidth Collision & congestion
Multicasting | Geocast | One-to-X, using geographic address | Mobicast, ROVER, ZOR | Efficient routing Less network consumption | bandwidth
 | Cluster | Cluster + head | COIN, CBDRP | Less packet delivery | Dividing group Select head
Notes: 1. Patel B, Shah K. A Survey on Vehicular Ad hoc Networks[J]. IOSR Journal of ComputerEngineering (IOSR-JCE) Vol, 2013, 15: 34-42.

## Slide 21: Research Fields
Networking Services
  Routing Protocols
    Routing Information based classification[1]
AODV[2]
DSR
…
FSR
DSDV
OLSR
ZRP
…
Topology Based Protocols
Proactive
Reactive
Hybrid
Position Based Protocols
Routing Protocols
Notes: 1. Marwa Altayeb, Imad Mahgoub, “ A Survey of Vehicular Ad hoc Networks Routing Protocols,” ISSR Journals, 2013, Vol. 3, No. 3, pp. 829-846.
2. Perkins, C. E. And Royer, E. M. (1999), “Ad-Hoc On-Demand Distance Vector Routing,” Proc. IEEE WMCSA ‟99, New Orleans, LA, Feb. 1999 ,pp. 90-100.

## Slide 22: Research Fields
Networking Services
  Routing Protocols
    Routing Information based classification
Position Based Protocols
Routing Protocols
Topology Based Protocols
Classified by forwarding/recovery strategies
Greedy Forwarding
Improved Greedy Forwarding
Direction Greedy Forwarding
Predictive Directional Greedy
Right-hand rule
Carry-and-forward
Path-recalculation
Forwarding Strategies[1]
Recovery Strategies[2]
Notes: Sardar Muhammad Bilal, Carlos Jesus Bernardos, Carmen Guerrero; Position-based routing in vehicular networks: A survey; Journal of Network and Computer Applications 36(2013) 685-697.
Fonseca A,Vazao T. Applicability of position-based routing for VANET in highways and urban environment. Journal of Network
and Computer Applications JNCA1084-8045 2009.

## Slide 23: Research Fields
Networking Services
    Routing Protocols: Comparison of Position based protocols
Protocols | Forwarding Strategy | Traffic Awareness | Recovery Strategy | Simulator Scenario
GPSR | Greedy | N | Right-hand-rule | Highway
GSR | Greedy along path | N | Greedy | Urban
A-STAR | Greedy along path | Y | Recalculate path | Urban
GPCR | Restricted Greedy | N | Right-hand-rule | Urban, Real city model
GyTAR | Improved Greedy | Y | Carry & Forward | Urban
DGR | Directional Greedy | N | Carry & Forward | Highway
PDGR | Predictive Directional greedy | N | Carry & Forward | Highway
Notes: 1. . Marwa Altayeb, Imad Mahgoub, “ A Survey of Vehicular Ad hoc Networks Routing Protocols,” ISSR Journals, 2013, Vol. 3, No. 3, pp. 829-846.

## Slide 24: Research Fields
Networking Services
  Security [10]:
  Contradictory properties
    Authentication & Liability
      Masquerade attack & denial of behavior
    Privacy & Anonymity
      Eaversdrop
      Leakage of identity info
        (location & movement patterns)
Physical Layer
Networking Services
LLC SubLayer
MAC SubLayer
Upper Layers
Security

## Slide 25: Research Issues
Networking Services
  Security [10]: Schemes
    Certification Authorities(CAs)
      The issue of certificate revocation[35]
    Use Keys
      Use pseudonym to improve privacy[33][34]
      Use asymmetric cryptography for safety message

## Slide 26: Research Issues
Networking Services
  Security: the Status Quo
    Lack of specification for a real security system
    Lack of performance evaluation

## Slide 27: Research Fields
Networking Services
  QoS Support
    Reliability
    Low Loss Rate
    Bounded Delay
Low Collision Rate
…
Physical Layer
Networking Services
LLC SubLayer
MAC SubLayer
Upper Layers
Routing Protocols
QoS Support
Mobility Model & Simulation

## Slide 28: Research Fields
Internal Layers
  QoS Requirements
    Reliability
    Low Loss Rate
    Bounded Delay
Low Collision Rate
    IEEE 802.11 P
…
TDMA based Protocols
Current Standard Solutions
Alternative Solutions
?
Notes: Hadded M, Muhlethaler P, Laouiti A, et al. TDMA-Based MAC Protocols for Vehicular Ad Hoc Networks: A Survey, Qualitative Analysis, and Open Research Issues[J]. Communications Surveys & Tutorials, IEEE, 2015, 17(4): 2461-2492.
      Re-broadcast to achieve reliability[14]
      Change the transmission range of the emergency messages[15]

## Slide 29: Research Fields
Networking Services
  Mobility Model & Simulation
Physical Layer
Networking Services
LLC SubLayer
MAC SubLayer
Upper Layers
Routing Protocols
QoS Support
Mobility Model & Simulation

## Slide 30: Research Fields
Networking Services
  Mobility Model & Simulation[1]
Traffic Simulator
Vehicular Trace
Generation
Network
Simulator
Communication Generation
Traffic Simulator
Vehicular Trace
Generation
Network
Simulator
Communication Generation
Embedded Network & Traffic Simulator
Isolated Network & Traffic Simulator
Notes: Härri J, Filali F, Bonnet C. Mobility models for vehicular ad hoc networks: a survey and taxonomy[J]. Communications Surveys & Tutorials, IEEE, 2009, 11(4): 19-41.

## Slide 31: Research Fields
Networking Services
  Mobility Model & Simulation
    Normal Schemes:
      Output (trace files) can be used as input for a network simulator (NS-2/3) [2] :
        MOVE[1]: Java + SUMO
      Integrate with network simulator:
        TraNs[4]: Java + SUMO + NS2
        NCTUNS[5]: C++ + GUI Support
Notes: H. Füßler, M. Torrent-Moreno, M. Transier, R. Krüger, H. Hartenstein, and W. Effelsberg, “Studying vehicle movements on highways and their impact on ad- hoc connectivity,” in ACM Mobicom 2005, Aug. 2005.
“U.S. Census Bureau. TIGER, TIGER/Line and TIGER-Related Products,” http://www.census.gov/geo/www/tiger/.
Sherali Zeadally, Ray Hunt, Yuh-Shyan Chen, Angela Irwin, Aamir Hassan, Vehicular ad hoc networks (VANETS): status, results,
and challenges, Telecommum Syst, 2010
4. Piorkowski M, Raya M, Lugo A L, et al. TraNS: realistic joint traffic and network simulator for VANETs[J]. ACM SIGMOBILE mobile computing and communications review, 2008, 12(1): 31-33.
5. Wang S Y, Lin C C. NCTUns 6.0: a simulator for advanced wireless vehicular network research[C]//Vehicular Technology Conference (VTC 2010-Spring), 2010 IEEE 71st. IEEE, 2010: 1-2.

## Slide 32: Research Fields
Networking Services
  Mobility Model & Simulation
    VANET Mobility Model Classification
Mobility Model for VANETs
Synthetic Model[1]
Survey-based Model
Trace-based Model[12]
Traffic Simulator-based Model
Udel[2]
Agenda-based[3]
ETH [4]
      Street Random WayPoint[11]
RWP[5]
PARAMICS[5]
CORSIM [6]
VISSIM [7]
SUMO [8]
CrawDaD[9]
UMASSDiesel- Net[10]
Notes: Khope S S, Gayakwad S V, Dhagdi S T. Vehicular Mobility Simulation For VANET[J]. International Journal of Advanced Research in Computer Science, 2013, 4(6).
UDel Models For Simulation of Urban Mobile Wireless Networks, http: //udelmodels.eecis.udel.edu/
Q. Zheng, X. Hong, and J. Liu, ”An Agenda-based Mobility Model” in Proc. 39th IEEE Annual Simulation Symposium (ANSS-39-2006), Huntsville AL , April 2006.
Realistic Vehicular Traces http://lst.inf.ethz.ch/ad-hoc/car-traces
Paramics: Microscopic Traffic Simulation, http://www.paramics- online. com/
CORSIM: Microscopic Traffic Simulation Model, http://www- mctrans. ce.ufl.edu/featured/TSIS/Version5/corsim.htm
ptv simulation - VISSIM, http://www.english.ptv.de/cgi- bin/traffic/traf vissim.pl
SUMO - Simulation of Urban Mobility, http://sumo.sourceforge.net
Community Resource for Archiving Wireless Data At Dartmouth (Craw- dad), http://crawdad.cs.dartmouth.edu
UMass Diverse Outdoor Mobile Environment (DOME), http://prisms.cs.umass.edu/dome
H. Füßler, M. Torrent-Moreno, M. Transier, R. Krüger, H. Hartenstein, and W. Effelsberg, “Studying vehicle movements on highways and their impact on ad- hoc connectivity,” in ACM Mobicom 2005 Aug. 2005.
V. Naumov, R. Baumann, and T. Gross, “An evaluation of inter-vehicle ad hoc networks based on realistic vehicular traces,” in MobiHoc ’06: Proceedings of the 7th ACM International Symposium on Mobile Ad Hoc Networking and Computing, pp. 108–119, 2006.

## Slide 33: Research Fields
Networking Services
  Mobility Model & Simulation
    The Status Quo:
      Integrated simulators coupling traffic and networks is in development.
      Specifications of APIs for coupling traffic flow and networking simulators are in need.
Traffic Simulator
Vehicular Trace
Generation
Network
Simulator
Communication Generation
Communication Interface
Traffic
Feedback
Network
Feedback

## Slide 34: Questions & Challenges
Scalability of VANET
  Bandwidth limitations, processing power, transmission frequency
  A long way to go to achieve high take-up level
Multi-channel synchronization in MAC Layer
  Single transceiver per vehicle
  Co-channel interference problem
How to Cope with Sparse and Partitioned Network in Initial Deployment?
  Use mobility to counterbalance sparsity[21]
    Require GPS and map info
  Existing solutions in MANET may help [22]

## Slide 35: Questions & Challenges
How to Re-design IP Stacks for VANET Networks?
  TCP/IP Stack is designed for wired network and is inadequate for MANET or VANET[32].
  CB MANET aims to build completely new IP Stacks[23].
How to Reach a Consensus on Other Stacks?
  TCP/IP is ubiquitous.
  Applications for VANETs have not been clearly defined yet.

## Slide 36: Questions & Challenges
How to Cope with High Node Density?
  Traffic jam or accident happens
  Solutions in wired network cannot handle spatial reuse
  Slotted approaches [12][13]
How to guarantee Connectivity?
  Connectivity is a real challenge due to high mobility of nodes
    Parition and merge of networks due to high mobility of nodes
    Predicting and message queuing [19][20]
    Mobility increases throughput in MANET[15]
How to support Time-Critical Traffic?
  Current WLAN solutions have no time constraints
  Broadcast storm during transmitting emergency message
  Existing solutions(Number, rate, range)
    Rebroadcast to achieve reliability[14]
    Change the transmission range of the emergency messages[15]

## Slide 37
Thank You

## Slide 38: References
“Vehicle-to-Vehicle”, https://en.wikipedia.org/wiki/Vehicle-to-vehicle
“PATH,” www.path.berkeley.edu
“USDoT ITS program,” www.its.dot.gov/factsheets/connected_vehicles_work.htm
“SAFESPOT,” www.safespot-eu.org
“ComprehensivePlanforITSinJapan”, www.mlit.go.jp/road/ITS/topindex/topindex_g06_2.html
“China ITS Industry Alliance”, http://www.c-its.org/
http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=4450627&url=http%3A%2F%2Fieeexplore.ieee.org%2Fxpls%2Fabs_all.jsp%3Farnumber%3D4450627
Hybrid VANET Network…
Routing: Ad Hoc …
http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=1306972&url=http%3A%2F%2Fieeexplore.ieee.org%2Fiel5%2F8013%2F29015%2F01306972
H. Hartenstein et al., “Position-Aware Ad Hoc Wireless Net- works for Inter-Vehicle Communications: The FleetNet Project,” MobiHoc ’01: Proc. 2nd ACM Int’l. Symp. Mobile Ad Hoc Net- working & Computing, New York: ACM Press, 2001, pp. 259–62.
https://users.ece.cmu.edu/~sazimi/SAE2011.pdf

## Slide 39: References
J. Blum, “Adaptive Space Division Multiplexing: An Improved Link Layer Protocol for Inter-Vehicle Communication,” IEEE Int’l. Conf. WiMob 2005, vol. 3, 2005, pp. 22–24.
K. Dobashi, “Adaptive MAC Protocol for High-Load Inter- Vehicle Communication,” Wireless and Mobile Computing, Networking and Commun. Mag., vol. 44, no. 1, 2006, pp. 74–82.
L. Liu et al., “A Vehicle-to-Vehicle Communication Protocol for Cooperative Collision Warning,” 1st Annual Int’l. Conf. Mobile and Ubiquitous Systems: Networking and Services, MOBIQUITOUS 2004.
M. Torrent-Moreno, P. Santi, and H. Hartenstein, “Fair Shar- ing of Bandwidth in VANETs,” Vehicular Ad Hoc Networks, 2005.
M. Grossglauer and D. N. C. Tse, “Mobility Increases the Capacity of Ad Hoc Wireless Networks,” IEEE/ACM Trans. Net., vol. 10, no. 4, 2002, pp. 477–86.
L. Viennot, P. Jacquet, and T. Clausen, “Analyzing Control Traffic Overhead Versus Mobility and Data Traffic Activity in Mobile Ad-Hoc Network Protocols,” Wireless Networks, vol. 10, no. 4, 2004, pp. 447–55.
I. Stojmenovic and X. Lin, “Power-Aware Localized Routing in Wireless Networks,” IEEE Trans. Parallel and Distributed Sys- tems, vol. 12, no. 11, 2001, pp. 1122–33.
K. Wu and J. Harms, “Performance Study of Proactive Flow Handoff for Mobile Ad Hoc Networks,” Wireless Networks, vol. 12, no. 1, 2006, pp. 119–35.
H. Menouar, M. Lenardi, and F. Filali, “Improving Proactive Routing in VANETs with the MOPR Movement Prediction Framework,” Proc. 7th Int’l. Conf. Intelligent Transport Sys- tems, 2007, pp. 438–43.
H. Wu, R. Fujimoto, R. Guensler, and M. Hunter, “MDDV: A Mobility-Centric Data Dissemination Algorithm for Vehicular Networks,” Vehicular Ad Hoc Networks, 2004.

## Slide 40: References
M. M. B. Tariq, M. H. Ammar, and E. W. Zegura, “Message Ferry Route Design for Sparse Ad Hoc Networks with Mobile Nodes,” MobiHoc, 2006, pp. 37–48.
“Control-Based Mobile Ad-Hoc Networking Program,” 2005; http://www.darpa.mil/sto/solicitations/CBMANET
V. Namboodiri, M. Agarwal, and L. Gao, “A Study on the Feasibility of Mobile Gateways for Vehicular Ad-Hoc Net- works,” Proc. VANET’04, 2004.
R. Wakikawa et al., “Design of Vehicle Network: Mobile Gate- way for MANET and NEMO Converged Communication,” Proc. 2nd ACM Int’l. Wksp. Vehicular Ad Hoc Networks, ACM Press, 2005, pp. 81–82.
B. Ducourthial, Y. Khaled, and M. Shawky, “Conditional Transmissions: A Strategy for Highly Dynamic Vehicular Ad Hoc Networks,” Heudiasyc lab. UMR CNRS 6599, Université de Technologie de Compiégne, Tech. Rep., 2006.
“Car 2 Car,” http://www.car-to-car.org
J. Bransted and L. M. Kristensen, “Specification and Performance Evaluation of Two Zone Dissemination Protocols for Vehicular Ad-Hoc Networks,” anss, vol. 0, 2006, pp. 68–79.
R. Fracchia, “Knowing Vehicles Location Helps Avoiding Broadcast Packets Storm,” PerCOMW, vol. 0, 2006, pp. 118–23.

## Slide 41: References
S. Ghandeharizade, S. Kapadia, and B. Krishnamachari, “PAVAN: A Policy Framework for Content Availability in Vehicular Ad-Hoc,” Vehic. Ad Hoc Networks, 2004.
T. Repantis and V. Kalogeraki, “Data Dissemination in Mobile Peer-to-Peer Networks,” Mobile Data Management, 2005.
Revealing TCP Unfairness Behavior in 802.11 Based Wireless Multi-Hop Networks, vol. 2, 2001.
P. Papadimitratos et al., “Architecture for Secure and Private Vehicular Communications,” Proc. 7th Int’l. Conf. Intelligent Transport Systems, 2007, pp. 339–34.
J. Freudiger et al., “Mix-Zones for Location Privacy in Vehicu- lar Networks,” WiN-ITS, 2007.
S. Miscali, “Efficient Certificate Revocation, MIT Laboratory for Computer Science, “ Tech. Rep. TM-542b, Mar. 1996, Tech. Rep.
J. Broch, D.A. Maltz, D.B. Johnson, Y.-C. Hu, and J. Jetcheva, “A performance comparison of multi-hop wireless ad hoc network routing protocols,” in Mobile Computing and Networking, pp. 85–97, 1998.
“U.S. Census Bureau. TIGER, TIGER/Line and TIGER-Related Products,” http://www.census.gov/geo/www/tiger/.
H. Füßler, M. Torrent-Moreno, M. Transier, R. Krüger, H. Hartenstein, and W. Effelsberg, “Studying vehicle movements on highways and their impact on ad- hoc connectivity,” in ACM Mobicom 2005, Aug. 2005.
V. Naumov, R. Baumann, and T. Gross, “An evaluation of inter-vehicle ad hoc networks based on realistic vehicular traces,” in MobiHoc ’06: Proceedings of the 7th ACM International Symposium on Mobile Ad Hoc Networking and Computing, pp. 108–119, 2006.
H. Hartenstein et al., “Position-Aware Ad Hoc Wireless Net- works for Inter-Vehicle Communications: The FleetNet Project,” MobiHoc ’01: Proc. 2nd ACM Int’l. Symp. Mobile Ad Hoc Net- working & Computing, New York: ACM Press, 2001, pp. 259–62.

## Slide 42
USA V2V | Europe V2I | China & Japan V2V&V2I
PATH[2], ITS[3] Awareness-based Improve safety | C2C CC27] SAFESPOT[4], FleeNet[40] Event-based Improve Mobility | Japan: JSK[5] China: CCSA[6] …

## Slide 43: Research Fields
Internal Layers
  Routing Protocols[8]
    Topology based (Ad hoc routing)[9]
    Position based (Geographical routing)[10]
      C2C CC uses geographic routing schemes[27]
      //Conditional transmission[26] is a generalization of this technology
      Scale well with dynamic network
      Optimizing routing path[18]
      More studies in need
    Cluster based
    Geocast

## Slide 44: Research Fields
Routing Protocols
For Comfort Applications
Unicasting
Multicasting
For Safety Applications
Broadcasting
Internal Layers
  Routing Protocols:
    From applications point of view

## Slide 45: Research Fields
Internal Layers
  Internet Connectivity
Application Layer
VANET Architecture
Routing Protocols
Internet Connectivity
Data Dissemination
QoS Support
Security
Models & Simulation
PHY/MAC Layer
Internal Layers
    Proactive & Reactive[17]

## Slide 46: Research Issues
VANET Networking
  Data Dissemination:
    Cannot use group address but node positions
    Safety applications: broadcast within a zone under all conditions
      Either use hop counts[28] or use vehicle location info[29]
      No comparison studies exist and further investigation is in need .
    Comfort application:
      Use infrastructure support [30]
      Build completely independent peer-to-peer system[31]

## Slide 47: Research Issues
VANET Networking
  Internet Connectivity
    Vehicles within a network
      Use multi-homed vehicles as gateways[24]
      Use infrastructure gateways
    Vehicles Crossing networks
      [25]